## Slide 1: Homotopy Continuation Meets GPU
Hongyi Fan
Cognex

## Slide 2: Motivation
Homotopy Continuation is simple
  Numerical method: Homotopy Continuation (HC) e.g. PHCpack，MiNuS, Julia and others
Simple and able to solve all sizes of problems;
Not efficient
Problem | HC Time with CPU w/o optimization | Elimination Template Solver
P3P | 40ms | 0.063ms
5 Points Relative Pose Problem | 60ms | 0.035ms
P4P unknown focal length and distortion | 130ms | 9ms
Notes: It relies on the simple and elegant idea to initially solve a simpler polynomial system (start system) and then deform its roots to the roots of the system we aim
to solve (target system) iteratively on the system parameter manifold

## Slide 3: Motivation
Accelerate HC with parallelization
  Multi-threading Path Tracking
    PHCpack
    Bertini
    Julia
    MiNuS
  Multi-threading Polynomial Evaluation in GPU
    PHCpack
Limited by number of CPU cores

## Slide 4: GPU-HC
Why GPU?
  GPU is becoming more and more powerful and available
    Computation power: Highly parallelized structure
    Portability: Jetson on micro aerial vehicles (drones)
GPU in multiview geometry tasks?
  Classic visual odometry
  Bundle Adjustment
  learning-based Multiview framework
  … and many others.
Jeon, Jinwoo, Sungwook Jung, Eungchang Lee, Duckyu Choi, and Hyun Myung. "Run your visual-inertial odometry on NVIDIA Jetson: Benchmark tests on a micro aerial vehicle." IEEE Robotics and Automation Letters 6, no. 3 (2021): 5332-5339.
Ren, Jie, et al. "MegBA: A GPU-based distributed library for large-scale bundle adjustment." European Conference on Computer Vision. Cham: Springer Nature Switzerland, 2022.
Zhang, Youmin, Fabio Tosi, Stefano Mattoccia, and Matteo Poggi. "Go-slam: Global optimization for consistent 3d instant reconstruction." In Proceedings of the IEEE/CVF International Conference on Computer Vision, pp. 3727-3737. 2023..

## Slide 5: GPU-HC
How to parallelize HC?
What are the bottlenecks in HC?
  Number of Solutions (homotopy paths)
  In each homotopy path…
    Prediction
    Correction
Solving a linear system
Jacobians and homotopy computation/evaluation
Cost 80~90% of the total time

## Slide 6: GPU-HC
How to parallelize HC?
Parallelization in different levels
  Path tracking parallelization
    Tracking simultaneously
  Fast linear system solving
    What GPU is good at
  Evaluation of complicated Polynomial & Jacobian

## Slide 7: GPU-HC
How to parallelize HC?
Path Tracking Parallelization
  Parallelize the “outer” part:
Assign 1 track to 1 warp (32 threads)
We need to assign 1 track to multiple threads for (1) lower level parallelization (2) always access to fast memories
Cannot assign a lot: thread synchronization takes time
Solution Tracking
The parallelism is organized in terms of thread blocks (TBs)
Each TB is composed of multiple threads running in groups of 32 (a warp)

## Slide 8: GPU-HC
What are the parallel computations in GPU-HC?
  Parallelize the “inner part” of each track
    cuBLAS, MAGMA
    Collaborate with the MAGMA library Developers
      High speed linear system solving for small matrix (dimension < 32x32)
      Fused Kernel
Dong, Tingxing, Azzam Haidar, Piotr Luszczek, Stanimire Tomov, Ahmad Abdelfattah, and Jack Dongarra. Magma batched: A batched BLAS approach for small matrix factorizations and applications on gpus. Technical Report. Technical report, 2016.
Solving a linear system
Notes: With the answers to the above two questions, we arrive at a nested parallelism for homotopy continuation.
In the fine level, we parallelize the inner part computation of each homotopy path. We tackle the two bottlenecks, namely, the linear system solver, and Jacobian/homotopy computation and evaluation.
Triangular solve of L portion is done in decomposition process

## Slide 9: GPU-HC
What are the parallel computations in GPU-HC?
  Fine level: Parallelize the “inner part” of each track
Jacobians and homotopy computation/evaluation
Parameter homotopy:
Compute the coefficients by
Constant in runtime
Notes: For the computation and evaluation of the Jacobians and homotopy, we make use of the idea of single instruction multiple threads computation.
Here’s an example of two polynomial equations with two unknowns
What we need to do on the GPU side is to evaluate them

## Slide 10: Comparisons on Other Problems

## Slide 11: Take away messages
Checkout our GitHub Repository!
GPU-HC directly solving the original large, low-degree system efficiently.
GPU-HC opens a door for problems that were previously unsolvable or inefficient made practical in use.
Our publications:
Chien, Chiang-Heng, Hongyi Fan, Ahmad Abdelfattah, Elias Tsigaridas, Stanimire Tomov, and Benjamin Kimia. "GPU-based homotopy continuation for minimal problems in computer vision." In Proceedings of the IEEE/CVF Conference on Computer Vision and Pattern Recognition, pp. 15765-15776. 2022.
Chien, Chiang-Heng, Hongyi Fan, Ahmad Abdelfattah, Elias Tsigaridas, Stanimire Tomov, and Benjamin Kimia. "Parallel path tracking for homotopy continuation using GPU." In Proceedings of the International Symposium on Symbolic and Algebraic Computation. 2022.
Ding, Yaqing, Chiang-Heng Chien, Viktor Larsson, Karl Åström, and Benjamin Kimia. "Minimal Solutions to Generalized Three-View Relative Pose Problem." In Proceedings of the IEEE/CVF International Conference on Computer Vision, pp. 8156-8164. 2023.

## Slide 12: Thanks for your attention